## Slide 1: Radiation Memory Test RIT Space Exploration T.J. Tarazvits, Austin Bodzas, James Lewis, Helen O’Connell
Acknowledgements
This work was supported by Boeing, USEED@RIT, Provost’s Learning Innovation Grant, Kate Gleason College of Engineering and the RIT Office of the President. Special thanks to Multidisciplinary Senior Design Director, Dr. Elizabeth DeBartolo and SPEX advisors Dr. Mihail Barbosu, Dr. Dorin Patru and Dr. Jennifer Connelly.
Objective
Components
Current Progress
G
Plans for the Future
If chosen to fly on SPEX’s cubesat mission, we plan on converting our proof of concept to a desktop prototype of the flight board. We would switch from the Arduino family to a TI MSP430, our leading option for our avionics board. Our development board would integrate PCM chips, either from the semiconductor industry or from RIT’s Microelectronics lab. We would also move away from breadboard prototyping to custom PCBs to validate board layouts. We would validate the functionality and durability of our designs with testing on the MSD vibration test stand and as a payload on the HAB program. A critical part of our experiment test plan is onboard error checking of stored data. Communications bandwidth is limited on orbit, so we are looking into sending telemetry on reported differences.
Create a technology demonstrator to validate new forms of computer memory such as Phase Change Memory(PCM) in the space environment. Our current goal is compare the read/write performance and radiation resistance of PCM to traditional flight proven memory types such as StaticRAM, MagneticRAM, and DynamicRAM.
Arduino Uno
Custom Breadboard
256K SPI Bus Serial EEPROM
256K SPI Bus Low-Power Serial SRAM
This semester we produced a proof-of-concept demonstration for ImagineRIT. Our test setup consists of an Arduino Uno microcontroller to control reading and writing to two different memory chips. We are using Commercial off the Shelf EEPROM and SRAM chips for their low cost and ease of use with existing software libraries. The controller dynamically generates and stores data into each chip. Radiation damage is simulated by random writes by the microcontroller across the chip. Also our visualization allows for manually changing the data on both chips.
G
The Problem
NASA has identified the flight readiness of PCM as a key area in their State of the Art of Small Satellites report. Due to the challenging thermal and radiation environment, and the mission critical importance of computer memory, it is difficult to build flight heritage of new memory types.