## Slide 1: VanGoBOT
An Assistive Drawing Device
Scan
Me!
Background
Art education is essential to giving students the ability to express themselves and be creative. Limited range of motion and other physical disabilities inhibit participation with traditional art utensils for students. Current methods such as hand-over-hand and tennis balls as adaptable grips are not always successful and offer limited independence to the student. VanGoBOT aims to help students with varying physical abilities engage and be more independent in their art expression.
.
P21068 from Left to Right:
George Heltz (ME), Dylan Lebedin (EE), Andrew Pasek (CE), Josh Kolosick (ME), John Owens (ME), Allison Morgan (EE), and David Nwokolo (CE).
Key
Met
Partially Met
Not Met
Results
Student Controlled Brush Strokes
Variety of Tools and Colors
30 Minutes of Use
Compatible with Standard Wheelchair
Interchangeable Control Interfaces
Dimensions
Easy Set-up and Take-down
Cost: At Budget
Portable
Weight
Mechanical System
Gripper
3D Printed Design
Servos open/close and raise claws
Accommodates different tool sizes
Belts/Motors
Move the gripper in x and y directions
Stepper motors to track location
Framework
PVC for smooth drawing surface
80/20 and T-nuts for structure during transportation
Plastic electronics enclosure
Magnetic sheet for paper attachment
Electrical System
Power and Control
Device plugs into the wall and converts to DC
Buck converters convert 12V to component voltages
Raspberry Pi controls servos and motors via motorPlate and code
Teacher Input
Programmed in Python, displayed on touch screen
Allows device set-up through inputting the paper size and changing the sensitivity of movement and pressure based on the tool
Can override student input if needed
Student Input
Easy Press Buttons or Joystick
4 Directions and start/stop
Velcro attachments for different input configurations
Acknowledgements
Client: Karen Knight, Art Educator, Orleans/Niagara BOCES Guide: Art North
Sponsor: Kids Miracle Making Club, Inc. RIT Resources: MSD Office, Shop Staff
Requirements