## Slide 1: Robotic Art Assist Manual

## Slide 2: Tensioning
To tension the belts loosen or tighten the labeled screws. The belts should be tight enough that the carriage moves without binding.
Grease can be applied to the bars labeled in order to help carriage movement. A small layer should be applied across the bar and then the carriage should be moved back and forth across the bar to ensure proper spreading.
The grease can be found here: https://www.amazon.com/dp/B0081JE0OO?psc=1&ref=ppx_yo2_dt_b_product_details

## Slide 3: Belt replacement
If the belts need to be replaced, they can be found at the two links provided below. In order to remove the belts you will need to first unscrew the pulley screws marked by the arrows. This will allow you to take the belt off of the pulley. The new belt should then be put on by first slipping over the gear and then screwing onto the pulley. The pulley can be loosened thru tensioning to allow the pin to be screwed on easier.
Short belt: https://www.mcmaster.com/6484K447/
Long belt: https://www.mcmaster.com/6484K451/

## Slide 4: Electronics/Cover
To remove the electronics cover start by removing the side covers by unscrewing the screws labeled by the arrows.
Then remove the all the feet. This will allow you to remove the electronics enclosure to change the fuses. Be careful as their are wires attached to the motors and other parts of the machine.

## Slide 5: Electronics/Cover
With the electronics cover removed you can unscrew the labeled fuses and replace them with the following fuses:
3A Fuse: https://www.grainger.com/product/MERSEN-Fuse-5LAZ3
3.2A Fuse: https://www.grainger.com/product/MERSEN-Fuse-5LAY1