## Slide 1: Camera Characterization
By: Liz Bondi, Tyler Shelley, Michaela Piel, Victoria Scholl, and Briana Neuberger
Notes: The hardware group decided to put together this presentation on how to characterize cameras to get a better understanding of what types of cameras might be useful for this project.

## Slide 2: Outline
I. Camera Characterization-what is it?
II. Resolution
III. Modulation Transfer Function (MTF)
IV. Tone Transfer Function (TTF)
V. Distortion
Notes: So first we're going to introduce the idea of camera characterization and explain what it is and provide a few examples.

## Slide 3: Camera Characterization
Some important camera characteristics include:
Spatial Frequency Response (SFR) data
limiting resolution
Fixed pattern noise in bright and dark images
focal length
zoom range
shutter lag
https://docs.google.com/a/g.rit.edu/viewer?url=http://dl.owneriq.net/3/36d147bd-0751-4dd6-8da5-55c0b455b74f.pdf&a=bi&pagenumber=1&w=504&h=693
Notes: Briana
Camera characterization is a technique used to determine the physical parameters of a camera and figure out which camera would be the most applicable to solve a task.
This second part is just a list of some of the camera characteristics we might consider testing for to determine what type of camera to use.
Spatial Frequency Response - provides a measurement of the capture of image spatial detail, which basically means they characterize the spatial interaction of neighboring signals whether they are in remote or close proximity. (closely related to MTF)
limiting resolution - measured by determining smallest group of bars, vertically and horizontally, for which the correct number of bars can be seen
Fixed pattern noise in bright and dark images/Dark-Signal Non Uniformity (DSNU) - variations of the dark signal from pixel to pixel which can be calculated as a function of exposure time and contributes to the visual image quality
Offset and readout noise -
focal length - how wide the camera can see
zoom range - determines how far the camera can see
shutter lag - how fast the camera responds

## Slide 4: Resolution: What is it?
image detail
# of pixels:
  1600x1200p
  1,920,000p
http://electronics.howstuffworks.com/cameras-photography/digital/digital-camera3.htm
Notes: Victoria
Resolution is the amount of detail in an image.
It is measured in LENGTH UNITS (smallest distance you can resolve), FREQUENCY UNITS (largest frequency you can resolve) pixels, often described by the width of pixels x height of pixels, or total pixels in the image (product of width and height). A megapixel is 1 million pixels, and the resolution of cameras is commonly described by the # of megapixels it has.
More pixels = more detail captured by camera = the larger its image can be made without becoming blurry or grainy.
more than # pixels, it's a system level parameter. factor in lens, sensor, etc.
THE RESOLUTION LIMIT (when you can no longer distinguish between points in an image) (in a telescope it's like how close can you bring two stars together before they blend together into one) = WHEN THE mtf = 0

## Slide 5: Why is it important?
http://artisticcommunication.com/?m=200909
11.1 MP
>1 MP
http://thinkbda.com/wp-content/uploads/2010/10/Thumbs-up.jpg
Notes: Victoria
There is a relationship between mtf and resolution. Roger? Elaborate?
Why does MTF matter?
To quantify the resolution of camera!
Resolution-
For security purposes, we need to be able to see details in our camera array's footage to identify people and things.
Resolution typically ranges from high quality (11.1 megapixels, top of the line digital cameras) to low (256x256 pixels).
We need to make sure that the images our array produces have sufficient resolution.

## Slide 6: MTF (Modulation Transfer Function)
Overview
Describes blurring action of lens on image
Measured by imaging calibrated targets

## Slide 7: Equation
fmax
fmin
gmax
gmin
gmax
gmin
fmax
fmin
fmax
fmin
http://lowfrequency.org/interactivity/wiki/index.php?title=Sonic_Processing_-_Sound_and_Music_in_Visuals
Notes: there are bright and dark places in images, and we can represent a simple version of this with a sine curve; the peaks are the bright parts and the troughs are the dark parts; you can see this on these three graphs where the scene is the first graph and the second graph is the image
amplitude of the g depends on the frequency of the f (when f has higher frequency, g gets averaged out more and amplitude is smaller) (modulation would be zero if it's a straight line on output gmax-gmin =0, so MT=0 at that frequency)
blur makes brights more bright, darks less dark
bright (peaks), dark (troughs): lens averages brightnesses, pushes it closer to the mean
when black, Amin=0 and mtf = 1
Note from María Helguera: Because you are calculating the Modulation Transfer Function. A is amplitude, not frequency. No need to guess, just look in a textbook,

## Slide 8: Measurement of MTF
http://www.psych.ucalgary.ca/pace/va-lab/Marcela/Assets/webreadypics/highlow.gif
Notes: this shows the modulation of the display: highest frequency bottom right, modulation is 0
Notes from María Helguera: You can also take a look at: http://rsbweb.nih.gov/ij/plugins/se-mtf/index.html

## Slide 9: Graph of MTF
Modulation
Oscillation Frequency (cycles/mm)
http://encyclopedia2.thefreedictionary.com/Resolving+Power+of+a+Photographic+System
Notes: Modulation plotted as function of oscillation frequency
low frequency, modulation is higher; higher frequency, modulation is lower (won't look right)
low pass filter (lens), attenuates high frequency (averages it out)
graph goes from 0 to 1 on the y-axis-it's the modulation, which is normalized
Note from María Helguera: Who is putting these slides together? There is no fun math, there is simply conversion of units. The maximum value in the vertical axis is 1 because the data are normalized

## Slide 10: Resolution and MTF: How do we measure it?
http://www.graphics.cornell.edu/~westin/misc/res-chart.html
http://www.distantfocus.com/projects/icis/images/AFref2.gif
Notes: Victoria
There are various tests we can perform when characterizing cameras and determining what their resolutions are.
Many of the tests involve patterns, more specifically resolving power test targets. (Image in slide = ISO [International Standards Organization] for measuring the resolution of digital still imaging. (Will this matter when we measure the resolution of video? Or not if we go frame by frame?)
  Those things cost a lot of money... the one above costs anywhere from $225 (printed size 200x356mm) to $950 (800x1422mm). [Edmund Optics http://www.edmundoptics.com/testing-targets/test-targets/resolution-test-targets/i3a-iso-resolution-test-chart/2287]
  (If you print them out yourself using your home printer, it will not be accurate for measuring resolution.)
  Luckily, we have some in the lab!
How to use:
Test shots MUST be set up perfect.
  Mount on tripod to avoid movement
  well lit
  Manual focus
  Contrast, saturation, etc must all be set to zero/neutral
HOW TO MEASURE RESOLUTION EXACTLY FROM CHART??
  Not only does it help us measure resolution, this chart serves as a good visual indicator of sharpness as well as CA (Chromatic Aberration) and distortion.
  take pictures of targets, measure max and min in the images with photoshop (find brightest/darkest pixels in a region), apply equations
File= most uncompressed type possible. (ideal- RAW)
more here: http://www.the-digital-picture.com/Help/ISO-12233.aspx
higher resolution systems, because they allow you to collect more details, will typically have a higher MTF

## Slide 11: Another Way
http://scien.stanford.edu/pages/labsite/2007/psych221/projects/07/camera_characterization/images/canon_res_target.jpg
Notes: you can do it all in one step but it's more complicated to explain and we'll learn about this later in our mtf class
Take picture of test target
Focus on "slant-edge" part
Open picture in Matlab
Run slant-edge program
Get MTF!

## Slide 12: TTF
TTF, or Tone Transfer Function, gives the average input and output data.
The lightness of the output is a function of the input.
TTF used to measure sensitivity and contrast.
Notes: This makes my head feel full of stupid. I would post the definition if it would help but...it doesn't. I'm currently attempting to find an e.l.i.5. explanation...I will clear out the notes section later if need be.
-Also here are some links:
-A slideshow, probably from rit as a imaging science type dude from rit is cited as the one source(dave kelbe, I may go hunt him down):
http://ife2010.wikispaces.com/file/view/Tone+Transfer+Function.pdf
-The definition of it. Good luck with comprehension:
http://www.digitizationguidelines.gov/term.php?term=tonetransferfunctionttf
Note from María Helguera: A little respect is required even in the notes section, what do you mean by "an imaging science type dude"?
May I suggest something? Open a textbook and read the appropriate sections. There are books in the lab that will help you understanding this material. Once you read the sections you will be able to write down suitable notes that will support a reasonable presentation.

## Slide 13: TTF Testing
http://tama.typepad.com/blog/2010/01/cri-leds-cmos-and-actually-getting-it-all-to-work.html
Notes: OK! Think I may be done? This is most everything I could find on the topic which wasn't much... Tell me if you think there is anything I can improve upon!
Note from María Helguera: obviously there is no understanding. What is the meaning of this target? How do you use it? What does it measure? whose notes are these? How could you even think you are done? Like I said in the previous page: open one of the textbooks in the lab and read the appropriate sections.

## Slide 14
http://www.imagescienceassociates.com/mm5/pubs/Performance_Taxonomy.pdf
Notes: Briana!

## Slide 15: What is Distortion?
Warping of lines in image from camera
due to spatial variation in magnification
http://www.dpreview.com/articles/5653763779/a-distorted-view-in-camera-distortion-correction
Notes: Free of distortion=orthoscopic
Reproduction scale is not the same through the whole image
changes image shape but not its color or sharpness

## Slide 16: Types of Distortion
Barrel
Pincushion
http://www.flickr.com/photos/tylerkellen/4400803013/
http://www.alpa.ch/glossary/photographic-know-how/distortion.html
Notes: Magnification is bigger closer to the optical axis- barrel
Magnification is farther away from the optical axis-pincushion
LOOK UP OPTICAL AXIS

## Slide 17: Distortion is Most Prominent In
Wide-Angle Lenses
Wide-Range Zoom
http://blog.photoshopcreative.co.uk/general/fix-barrel-distortion/
Notes: Little/no zoom usually results in a barrel distortion
Big amount of zoom usually results in a pincushion distortion (Try to find image example)
These lenses are difficult to make

## Slide 18: How to Fix Distortion
"Tilt and Shift" Lens
Software
  Calibrate lens to determine distortion map
  Calculate geometric correction
  Implement correction in software
Notes: Mickey
-to calibrate- take picture of graph
-

## Slide 19: How to Fix Distortion Example
http://www.flickr.com/photos/tylerkellen/4400803013/
http://www.dpreview.com/articles/5653763779/a-distorted-view-in-camera-distortion-correction
Notes: Mickey

## Slide 20: How it Relates
http://www.flickr.com/photos/tylerkellen/4400803013/
Notes: Talk about Go Pro