## Slide 2: Digital Cameras (Basics)
CCD (charge coupled device): image sensor
Resolution: amount of detail the camera can capture
Capturing Color: filters go on sensor
Digital Camera Exposure and Focus
  A digital camera has to control the amount of light that reaches the sensor- they do this using aperture and shutter speed
    Aperture: size of the opening in the camera (most digital cameras have automatic apertures, but professional/hobby can have manual adjustment)
    Shutter speed: amount of time that light can pass through the aperture (digital)
  Camera has to adjust the lenses to control how the light is focused on the sensor
  Focal length: distance between lens and the surface of the sensor
  Here’s a few options for zooming:
    Optical zoom: change the focal length of the lens rather than magnify the info that hits the sensor
    Digital zoom: camera takes pixels from center of image sensor and interpolates them to make a full-sized image

## Slide 3: Sensor: Charge Coupled Device (CCD)
Notes: converts light into electrons, charge is eventually converted to binary

## Slide 4: Resolution and Pixel Size
Pixel: picture element, tiny squares of color that create an image
  The smaller the pixel and the higher the pixel count, the better the resolution
Resolution: # pixels detector can pick up
1296
964
Notes: Pixel: picture element
Tiny squares of color that create an image
Number of pixels in the image determines its pixel count
The smaller the pixel and the higher the pixel count, the better the resolution

## Slide 5: Video Data Output
The Chameleon is 8 bit or 16 bit
Bit (binary digit): smallest data unit in a computer
8 bit image can have 256 different shades of grey (28=256)
16 bit image can have 65,536 different shades of grey (216=65,536)
Colors are 8 bits for red, blue, and green (so 24 bits total)
Monochromatic: 256 shades of grey/8 bit image
Notes: Diagram: heat it more or less, brighter or darker
8 bit vs. 16 bit color cameras
More bits generally means better quality and processing
Our eyes can barely, if at all, tell the difference between 8 bit and 16 bit
16 bit images are much slower than 8 bit images

## Slide 6: Image Data Formats
How does a camera get its color?
  A Bayer filter is put on the sensor!
    It blocks or absorbs certain wavelengths based on the color on the filter
    The sensor still picks up the intensity, so that gives you different shades of colors

## Slide 7: Transfer Rates
How quickly bits of data can be processed or transmitted by a device
Usually mega or kilo-bits per second
Measured in bits per second (bit/s)

## Slide 8: The Chameleon
Specification | Chameleon’s Info.
Image Sensor Type | CCD
Maximum Resolution | 1296(H) x 964(V)
Pixel Size | 3.75μm x 3.75μm
Video Data Output | 8, and 16-bit digital data
Image Data Formats | Bayer data (color models)
Digital Interface | 5-pin Mini-B USB 2.0 digital interface for camera control, video data transmission, and power
Transfer Rates | 480 Mbit/s
General Purpose I/O Ports | 7-pin GPIO connector
Size | 44mm x 25.5mm x 41mm and 37 grams
Lens Mount | CS-mount (5mm C-mount adapter included)

## Slide 9: Sensors- Color Model
Arbitrary units on y-axis
Normalized – relative to the maximum
Highest response is 1.0
Wavelength in nm on x-axis
Blue, green, red graphs
If light has wavelength of 450nm, the blue and green sensors on the Bayer filter will pick up the radiation

## Slide 10: Sensors- Monochrome Model
Once again, normalized y-axis
Arbitrary units y-axis
Wavelength on x-axis in nm
Grayscale
Mostly visible light
Some infrared light toward right side of x-axis
Peaks around 600nm

## Slide 11: GPIO
The General Purpose I/O (GPIO) connector is used to power the camera externally and transfer data

## Slide 12: Multi Camera Array with Point Grey (Company Example)
May need to use Grasshoppers
Software comes with it (Multisync-we already have FlyCapture)
Power: host adapter, Firewire, or GPIO port
Use daisy chaining to connect the cameras
16 can be connected to a laptop
32 can be connected to one PC
Notes: https://mail-attachment.googleusercontent.com/attachment/u/0/?ui=2&ik=6cd7f4612d&view=att&th=139c00acc61966d2&attid=0.1&disp=inline&realattid=f_h71yedza0&safe=1&zw&saduie=AG9B_P_wc859w83OgzLbXvcIOtvW&sadet=1347639554842&sads=Tf99SZkDzzjK9O1W1vrE_Mi8ceY

## Slide 13: Daisy Chaining
Reduces clutter
Can connect cameras together
23 cameras can be daisy chained
If the first camera fails, they all fail

## Slide 14
Notes: The 4 adapters are FirePRO 3-port hubs
2 firewire 1394 PCI Express cards

## Slide 16: Summary
CCD sensor – charge coupled device
USB digital interface
GPIO – powers device and transfers data
Bayer color filter
Can be used in a multi camera array
Good equipment to begin testing
Could be used in a design in the future

## Slide 17: The End
Questions?