## Slide 2: Definitions
Megarays - number of light rays captured by the light field sensor.
Plenoptic - camera that uses a mirrolens array to capture 4D light field information about a scene.

## Slide 4
Photographs do not record most of the information about the light entering the camera.
Light field cameras shows how light coming from one part of the lens differs from the light coming from another. (Vectors of light, where they originate, and how they are manipulated using lenses)
Light fields are defined in a couple different ways, one is as the geometrical distribution of light rays flowing in space.
The total geometric distribution of light as a plenoptic function over the 5D space of rays – 3D for each spatial position and 2D for each direction of flow.
Latin plenus for complete or full
Complete/Full Sight
Optic meaning sight
+
=

## Slide 5
5D Plenoptic Function
The light field at any point in space as a 5D function.

## Slide 6
Multiple vectors originating
from one point

## Slide 8: What is a Lytro Camera?
Plenoptic camera that has a main photographic lens, a micro-lens array and a digital photosensor
Captures the light field of an image to replicate it with the ability to refocus the image afterwards

## Slide 9: Camera Specifications
Camera Type | Point-and-shoot
3D Capture | Stills
Light Field Sensor Size | 6.5x4.5mm
Storage Type | Internal Samsung Flash Memory
Lens | 8x zoom, f/2 constant
File Output | Light field picture file (.lfp)
Light Field Resolution | 11 Megarays
Video capability | None
Processor | Zoran ZR36246BGXX
Picture Output | HD quality, “living pictures”

## Slide 10: What is inside the Lytro Camera?
Lens Array
Light Field Sensor
Light Field Engine
Marvell Avastar 88W8787 SoC - a chip that offers WiFi and Bluetooth capabilities (which is not in use quite yet)

## Slide 12: Light Field Engine 1.0
processes the light ray data captured by the sensor.
It “travels with every living picture, letting refocus happen on the camera, desktop and online.”

## Slide 13: Light Field Sensor
CMOS Sensor - common in cameras, convert light into electrons and place it into a cell. It then reads the values in each cell and changes it to a digital value.
Micro-lens array - attached to a standard sensor, it divides the pixels from the CMOS into areas, showing the image at different angles.

## Slide 14: Primary Lens Array
8x optical zoom and f/2 lens
Aperture is constant to allow for the same range of light capture during zoom

## Slide 15
The blue lines on the left represent the light field acquired in one pixel of an image. Its location corresponds to the blue line on the ray-space diagram

## Slide 17: Lytro Camera
Photo sensor

## Slide 18: Proto type

## Slide 19
With the Lytro no light rays are cutoff.

## Slide 20: Raw Light Field
Notes: each small circle is caused by a micro-lens in the array
take sample pixel from each lens, combine to create full image
<number>

## Slide 21: Matching f/ ratio
Notes: larger aperture (f/8) leaves wasted space
smaller aperture (f/2.8) causes overlap
minimizes unused space
eliminates overlap between micro lens images
forces fixed lens aperture
<number>

## Slide 22: Software Steps
demosaicking
correct for lateral misalignment
shift and sum sub-aperture images
Notes: demosaicking to extract RGB values
misalignment between micro-lens array and sensor
<number>

## Slide 23: Digital Refocusing
Original
Refocus
Notes: camera auto-focus on hair (10 cm misfocus)
light field allows for refocusing in software
<number>

## Slide 24: Impressions
Advantages
highly portable
refocusing ability
Disadvantages
reduced total resolution
fixed aperture
Notes: more mobile than camera array
decreased control over lighting
lenses decrease effective pixel count (resolution)
<number>