## Slide 1: Everything You Ever Wanted to Know About Optics
Liz Pieri, Victoria Scholl,
Joe Allen, Dan Chalifoux

## Slide 2
In all cameras, light enters through the lens and hits the recording medium. (In film cameras, the film plane, in digital cameras (for our purposes), the sensor.)
<http://www.mediacollege.com/photography/introduction/>

## Slide 3
The distance between the lens and the sensor is called the focal length (in mm).
Focal length determines angle of view (measured in degrees), also known as field of view: meaning what the lens and camera can capture, from left to right and top to bottom.
<http://www.trustedreviews.com/opinions/digital-photography-tutorial-focal-length>

## Slide 4
Focal Length
Demo 1: Overhead Projector

## Slide 5
Focal Length
Demo 2: Big light & lens

## Slide 6
Lenses with different focal lengths have different angles of view.
Different combinations of lenses result in different properties.
<http://paulbourke.net/miscellaneous/lens/>

## Slide 7
In general,
Wide Angle lenses have short focal lengths (i.e. 10mm), resulting in wide angles of view.
Telephoto lenses have long focal lengths (i.e. 75mm), resulting in narrow angles of view.
“Normal” or “Standard” lenses (with focal lengths similar to that of the human eye, i.e. 25mm or 50mm) are in between.

## Slide 8
Field of View Demo
Video Camera

## Slide 10
Depth of field (D.O.F.) is the distance between the nearest and furthest objects that appear to be sharply in focus in an image.
<http://timd-365-photos.blogspot.com/2009/11/november-13th-depth-of-field.html>
LEFT: Shallow (small) D.O.F. RIGHT: DEEP (large) D.O.F.

## Slide 11
F/22
F/5.6

## Slide 14
Lens Distortions are essentially the different degrees in which a given image can be misrepresented do to the physical imperfections and individualistic properties of the lens and/or combination of lenses being used to capture it.
<Undistorted Image>

## Slide 15
Barrel Distortion is a common, easy to digitally correct, type of geometric lens distortion prominent to wide angle lenses. This specific lens distortion bends strait lines spherically outwards from the center of the image.
<Barrel Distorted Image>

## Slide 16
Pincushion Distortion is another common, easy to digitally correct, type of geometric lens distortion, that is common to telephoto lenses. This specific lens distortion curves strait lines inwards, pinching the image tight in the center.
<Pincushion Distorted Image>

## Slide 17
Complex Distortion is comprised of both Barrel Distortion and Pincushion Distortion functioning in overlap. This sort of varied hybrid distortion pattern is present in most “real-world lenses,” such as common, household/recreational, non-specialty cameras.
<Complex Distorted Image>

## Slide 18: Aberrations

## Slide 19: Defocus

## Slide 20
<http://www.radiomaster.ru/reviews/view/292/>

## Slide 21: Comatic Aberration

## Slide 22
<http://en.wikipedia.org/w/index.php?title=File%3ALens-coma.svg&page=1>

## Slide 23
<http://www.olympusmicro.com/primer/java/aberrations/coma/index.html>

## Slide 24: Petzval Field Curvature

## Slide 25
<http://en.wikipedia.org/wiki/Petzval_field_curvature>

## Slide 26: Spherical Aberration

## Slide 27
<http://en.wikipedia.org/wiki/File:Spherical_aberration_2.svg>

## Slide 28
<http://upload.wikimedia.org/wikipedia/commons/1/10/Spherical-aberration-slice.jpg>

## Slide 29: Chromatic Aberration

## Slide 31: 2

## Slide 32
<http://www.dpreview.com/learn/?%2FGlossary%2FOptical%2Fchromatic_aberration_01.htm>

## Slide 33
<http://www.dpreview.com/learn/?%2FGlossary%2FOptical%2Fchromatic_aberration_01.htm>

## Slide 34: Demo(s)