## Slide 1: Geometric Calibration of Cameras
Liz Pieri, Kevin Sacca, Billy Frey, Amy Becker

## Slide 2: Background
Calibration is a way of examining a controlled image/video and deducing what the camera situation was at the time the image was captured
Can be used to figure out:
  location of camera in relation to a scene in a photograph
  focal length scene was shot at
  horizontal/vertical scaling factors
  shape of pixels
  skew factor
  lens distortion
Can be used to take an image sent to a computer and figure out various coordinates of the real world
Notes: Calibration used to be a tedious process, but modern software makes it easy to achieve
Liz

## Slide 3: Radial Distortion
Real lenses do not really image lines as lines, and with cheap lenses or with short focal lengths, there is significant error.
Notes: Liz

## Slide 4: Radial Distortion Modeling
Want to minimize the distance between distorted line and ideal line
(x',y') is a radial projection of (x,y) on a straight line
Notes: Liz

## Slide 5: Pinhole Camera Model
There is a fundamental assumption in our calibration method that the camera acts as a pinhole camera.
Notes: Billy

## Slide 6: Pinhole Camera Model
The pinhole camera model is only an approximation of what the 3D scene looks like
Geometric distortions (blurring of unfocused objects caused by lenses and finite sized apertures) are not taken into account
The quality of the camera affects the accuracy of the pinhole model
Notes: Billy

## Slide 7: Calibrating Using Caltech Website
Downloaded toolbox for matlab and sample pictures from website
Completed first tutorial on website for camera calibration with their 20 sample pictures
We took 30 pictures because more information can be analyzed by the computer when calibrating
Using 30 pictures gets rid of other variables that would be present with only 15 pictures, resulting in more accurate data
Sample pictures from website
Notes: Took 30 pictures because .... (MH)
Amy

## Slide 8: The Process
Print out and mount a grid
Take pictures of it tilted at numerous different positions and angles
Give the computer information about what it's seeing on the grid (size of boxes, number of boxes)
Then, you let matlab analyze the images and account for the error that the camera creates
At the end, matlab gives us the intrinsic parameters
These known intrinsic parameters are used to correct the error that the camera causes
We will now show you the process in matlab
Notes: Amy
DEMO BREAK

## Slide 9: Intrinsic Parameters
Focal length: The focal length in pixels is stored in the 2x1 vector fc.
Principal point: The principal point coordinates are stored in the 2x1 vector cc.
Skew coefficient: The skew coefficient defining the angle between the x and y pixel axes is stored in the scalar alpha_c.
Distortions: The image distortion coefficients (radial and tangential distortions) are stored in the 5x1 vector kc.
Notes: Amy

## Slide 10: Calibration results after optimization (with uncertainties)
Focal Length: fc = [ 4157.98585 4171.02467 ] ± [ 27.87620 28.51297 ]
Principal point: cc = [ 701.38591 575.64447 ] ± [ 47.94380 49.46080 ]
Skew: alpha_c = [ 0.00000 ] ± [ 0.00000 ] => angle of pixel axes = 90.00000 ± 0.00000 degrees
Distortion: kc = [ -0.05967 -6.10873 0.01049 -0.00232 0.00000 ] ± [ 0.10572 5.15735 0.00324 0.00260 0.00000 ]
Pixel error: err = [ 0.59055 0.63039 ]
Notes: This requires units and a bit of thought. Is focal length in centimeters? What's the meaning of accuracy and precision? Do you need so many decimal places? MH
This is the data cut and pasted from the matlab calibration, the decimal places are just what the program gives. Focal length is in pixels. I explain how you get to a focal length in millimeters on the next slide.
Kevin

## Slide 11: Calculations
The point grey chameleon has a pixel size of 3.75 micrometers, or 3.75 * 10^-6 meters.
So, with the focal length we have from the data, which is a focal length of 4157.98585 pixels.
(3.75 x 10-6 meters/pixel )(4157.98585 pixels) = 0.01559 meters = 15.59mm focal length.
Notes: Are you sure that focal length is measured in pixels? MH
that is what the caltech website says.
Kevin

## Slide 12
Our Grid Positions
Notes: Kevin

## Slide 13
Relative Camera Positions
Notes: Kevin

## Slide 14: Using the Intrinsic Parameters
Let P be a point in space of coordinate vector XXc = [Xc;Yc;Zc] in the camera reference frame.
Let us project now that point on the image plane according to the intrinsic parameters (fc,cc,alpha_c,kc).
Let xn be the normalized (pinhole) image projection:
Let r2 = x2 + y2.
After including lens distortion, the new normalized point coordinate xd is defined as follows:
where dx is the tangential distortion vector:
Notes: Amy

## Slide 15: Using the Intrinsic Parameters
Once distortion is applied, the final pixel coordinates x_pixel = [xp;yp] of the projection of P on the image plane is:
Therefore, the pixel coordinate vector x_pixel and the normalized (distorted) coordinate vector xd are related to each other through the linear equation:
where KK is known as the camera matrix, and defined as follows:
Notes: Amy

## Slide 16: Source
http://www.vision.caltech.edu/bouguetj/calib_doc/